## Slide 1: NY CREATES E-Characterization Program
4/11/2024

## Slide 2: High-Level Hierachy
eChar. dhAddRow
Main GUI
Main.py - Initialization
E-Characterization
Instruments
Results Window
Prober Window
Statistical Output Window
Results Handling
Instrument Control Thread
Main Thread
Result Handling Thread
Statistical Data Analysis Thread
Execution Thread
Start Execution
Start Execution
Configuration
copy
B1500A
B1530A
E5274A
Oscilloscope
Pulse Gen.
Prober
Matrix
Hand over control during execution
B1500A
B1530A
E5274A
Oscilloscope
Pulse Gen.
Prober
Matrix
eChar.plotIVData
eChar.dhValue
eChar.writeDataToFile
Data Generation and Manipulation
eChar.dhValue
StatisticalAnalysis
SaveData
Augment Data
Augment Data

## Slide 3: Tool Hierarchy
Folders:
Drivers
  Agilent.py
  B1500.py
  B1530.py
  ProbeStations.py
  ….
ElectricalCharacterization
  CV-Meas.py
  IV-Meas.py
  ReRAM.py
  Ferroelectric.py
  …
DieFiles
  Contains custom wafer maps
MatrixFiles
  Contains matrix Files
User Defined Measurement Routines
They rely on the tool driver for easy access to all underlying function
They use eChar class to interact with the program, save and plot data
Universal Wrappers using pyvisa and .dll to enable tool interactions and pre-define common function.
ADMIN access only

## Slide 4: eChar Class (E-Characterization)
Common functions:
dhValue(Value, Name, Unit)
  Creates a parametric value to perform statistical analysis and yield check on
dhAddRow(values, cycleStart=None, cycleStop=None)
  Passes a set of dhValue variables to create a row in a chart
  i.e. after each cycle or iteration of an execution one row gets added to a spreadsheet
plotIVData(data)
  Information to plot data in the result window
  Data is dictionary discussed later
eChar.LogData.put()
  Write an additional string to the log file
eChar.startThread(target=func, args=(,), **kwargs)
  Starts a thread from func with arguments args
  Thread will be added to list and managed by eChar
eChar.writeDataToFile(header, OutputData, startCyc=curCycle)
  Sends data to eChar to be written to the hard drive.
  Header is a list of strings
  OutputData is a 2-dimensional list of the output data

## Slide 5: Thank you
CONTACT: Karsten Beckmann
EMAIL: kbeckmann@ny-creates.org